# Test setups and proceedings for LoRa evaluation
## First test setup: Raw LoRa implementation
Data is collected as fast as possible and compared to prior set threshold limits. If the threshold limits are exceeded (positive or negative) the data is packed into a message, added to a queue and send via LoRa. The central receiver sends an acknowledgment if the CRC is correct, which leads to the message put into queue being deleted. If the queue contains ten elements and an eleventh one is added, the latest entry is popped.
Every sensorboard has an initial time.sleep() function call before the execution of the infinite loop, which is increased by one for each sensorboard added to the setup (first sensorboard 10 s, second sensorboard11 s, third sensorboard 12 s, fourth sensorboard 13 s).
## Second test setup: Raw LoRa implementation with re-transmission of packets
Same as the first test, with an additional re-transmission mechanism. After five seconds the queue is checked. If the queue has more than zero elements in it, the latest packet is retransmitted. After that is tried two consecutive times, the timer is deinitialized and restarted when another message is send.
## Third test setup: Raw LoRa implementation with re-transmission of packets and random back-off
As in the second test, with an additional random back-off mechanism. In this test case there is no time.sleep() call before the infinite loop execution. After a message is sent a random value between 0 and 1 is generated. If the values is greater than or equal to 0.4, the message sending interval and the re-transmission interval are randomized (message sending interval between 20 s and 40 s, re-transmission interval between 2 s and 10 s).

## Fourth test setup: Redundancy implementation
As in the third test, but with only two sensorboards. A third sensorboard is added as a redundant sensorboard sending heartbeat messages instead of data filled messages. After one of the boards stops working, the redundant sensorboard will start working as if it is a normal sensorboard. The commands for changing the behavior of the redundant sensorboard are issued by the router.
## Test proceedings 1
General setup: Distances in meters
	Router	Board #1	Board #2	Board#3	Board #4
Router	0	3.6	3.7	1	1.7
Board #1	3.6	0	1.2	-	2.7
Board #2	3.7	1.2	0	3.3	-
Board #3	1	-	3.3	0	2.7
Board #4	1.7	2.7	-	2.7	0

Test proceedings:
1. Let the boards run for 15 minutes and unplug board #1 and #2. After one minutes plug board #1 and # 2 in again. Let the boards run for another 60 minutes.
2. Let the board run for 6 minutes and unplug board #1 and #2. After one minute plug board #1 and #2 in again. Let the boards run for another 5 minutes. Perform this experiment with the threshold limits permanently broken.

Test for sensorboards with redundancy implementation: Let the sensorboards run for 5 minutes. After that unplug one non-redundant sensorboard. After another 5 minutes plug the sensorboard in again. Let the system run for a few more minutes.

## Test proceedings 2 (09.08.2022)
General setup: Rough distances in meters
	Router	Board #1	Board #2	Board#3	Board #4
Router	0	3.6	3.7	0.95	1.45
Board #1		0	1.2	3.3	2.7
Board #2			0	3.1	3.3
Board #3				0	2.0
Board #4					0

Setup note: All sending times were reduced by 75%, as well as the randomization intervals and the randomization step. The time when the status of the sensorboards is checked on the rbpi is reduced to 60 seconds.

Test proceedings:
1. Let sensorboards run for 15 min after starting simultaneously.
2. Let sensorboards #3 and #4 run for 16 min after starting simultaneously. One min after starting #3 and #4 start sensorboards #1 and #2 simultaneously. In total sensorboards #1 and #2 are running 15 min, one min less than sensorboards #3 and #4.
## Test proceedings 3 (starting 10.08.2022)
General setup: Rough distances as in Test proceedings 2.
Setup note: All sending time were halfed, as well as the randomization intervals and randomization step. The time when the status of the sensorboards is checked on the rbpi is reduced to 60 seconds.
Test proceedings:
1. Let sensorboards run for 60 min after starting simultaneously.
2. Let sensorboards #3 and #4 run for 61 min after starting simultaneously. One min after starting #3 and #4 start sensorboards #1 and #2 simultaneously. In total sensorboards #1 and #2 are running 60 min, one min less than sensorboards #3 and #4.